# Nalezy przede wszystkim opisac zapis informacji w SSD i magnetycznym dysku w oparciu o GMR. Można także wspomnieć o nowym sposobie zapisu przy uzyciu ferroelektrykow

# https://www.pcmag.com/article2/0,2817,2404258,00.asp

# SSD vs. HDD: What's the Difference?

Do you like your storage cheap and plentiful, or fast and safe? Here's how to choose between a traditional hard drive and a solid-state drive in your next PC.

PCMag reviews products independently, but we may earn affiliate commissions from buying links on this page. Terms of use.

## The Choice Is Yours

Until recently, PC buyers had little choice about what kind of storage to get in a laptop or desktop. If you bought an ultraportable, you likely had a solid-state drive (SSD) as the primary drive (C: on Windows, Macintosh HD on a Mac). Every other desktop or laptop form factor had a hard disk drive (HDD). Now, you can configure most systems with either an HDD or an SSD, or in some cases both. But how do you choose? We explain the differences between SSDs and HDDs (or hard drives), and walk you through the advantages and disadvantage of each to help you decide.

## HDD and SSD Explained

The traditional spinning hard drive is the basic non-volatile storage on a computer. That is, information on it doesn't "go away" when you turn off the system, as is the case with data stored in RAM. A hard drive is essentially a metal platter with a magnetic coating that stores your data, whether weather reports from the last century, a high-definition copy of the original Star Wars trilogy, or your digital music collection. A read/write head on an arm accesses the data while the platters are spinning.

An SSD does functionally everything a hard drive does, but data is instead stored on interconnected flash memory chips that retain the data even when there's no power present. These flash memory chips are of a different type than is used in USB thumb drives, and are typically faster and more reliable. SSDs are consequently more expensive than USB thumb drives of the same capacities. Like thumb drives, though, they're often much smaller than HDDs and therefore offer manufacturers more flexibility in designing a PC. While they can take the place of traditional 2.5-inch or 3.5-inch hard drive bays, they can also be installed in a PCIe expansion slot or even be mounted directly on the motherboard, a configuration that's now common in high-end laptops and all-in-ones.

Note: We'll be talking primarily about internal drives in this story, but almost everything applies to external hard drives as well. External drives come in both large desktop and compact portable form factors, and SSDs are gradually becoming a larger part of the external market.

## A History of HDDs and SSDs

Hard drive technology is relatively ancient (in terms of computer history, anyway). There are well-known photos of the IBM 650 RAMAC hard drive from 1956 that used 50 24-inch-wide platters to hold a whopping 3.75MB of storage space. This, of course, is the size of an average 128Kbps MP3 file today, in the physical space that could hold two commercial refrigerators. The RAMAC 350 was only limited to government and industrial uses, and was obsolete by 1969. Ain't progress great?

The PC hard drive form factor standardized at 5.25 inches in the early 1980s, with the 3.5-inch desktop-class and 2.5-inch notebook-class drives coming soon thereafter. The internal cable interface has changed from serial to IDE (now frequently called parallel ATA, or PATA) to SCSI to serial ATA (SATA) over the years, but each essentially does the same thing: connect the hard drive to the PC's motherboard so your data can be processed. Today's 2.5- and 3.5-inch drives mainly use SATA interfaces (at least on most PCs and Macs), though some high-speed SSDs use the faster PCIe interface instead. Capacities have grown from multiple megabytes to multiple terabytes, more than a million-fold increase. Current 3.5-inch hard drives have capacities as high as 10TB, with consumer-oriented 2.5-inch drives maxing out at 4TB.

The SSD has a much shorter history. There has always been an infatuation with nonmoving storage from the beginning of personal computing, with technologies like bubble memory flashing (pun intended) and dying in the 1970s and 1980s. Current flash memory is the logical extension of the same idea, as it doesn't require constant power to retain the data you store on it. The first primary drives that we know as SSDs started during the rise of netbooks in the late 2000s. In 2007, the OLPC XO-1 used a 1GB SSD, and the Asus Eee PC 700 series used a 2GB SSD as primary storage. The SSD chips on low-end Eee PC units and the XO-1 were permanently soldered to the motherboard. As netbooks and other ultraportable laptop PCs became more capable, SSD capacities increased and eventually standardized on the 2.5-inch notebook form factor. This way, you could pop a 2.5-inch hard drive out of your laptop or desktop and replace it easily with an SSD. Other form factors emerged, like the mSATA Mini PCIe SSD card, M.2 SSD in SATA and PCIe variants, and the DIMM-like solid-state Flash Storage in the Apple MacBook Air and MacBook Pro, but today many SSDs still use the 2.5-inch form factor. The 2.5-inch SSD capacity currently tops out at 4TB, but Seagate does offer a 60TB version for enterprise devices like servers.

## Advantages and Disadvantages

Both SSDs and hard drives do the same job: They boot your system, and store your applications and personal files. But each type of storage has its own unique feature set. How do they differ, and why would you want to get one over the other?

Price: SSDs are more expensive than hard drives in terms of dollar per gigabyte. A 1TB internal 2.5-inch hard drive costs between $40 and $50, but as of this writing, an SSD of the same capacity and form factor starts at $250. That translates into 4 to 5 cents per gigabyte for the hard drive and 25 cents per gigabyte for the SSD. Since hard drives use older, more established technology, they will remain less expensive for the near future. Those extra hundreds for the SSD may push your system price over budget.

Maximum and Common Capacity: Although consumer-based SSD units top out at 4TB, those are still rare and expensive. You're more likely to find 500GB to 1TB units as primary drives in systems. While 500GB is considered a "base" hard drive capacity in 2018, pricing concerns can push that down to 128GB for lower-priced SSD-based systems. Multimedia users will require even more, with 1TB to 4TB drives common in high-end systems. Basically, the more storage capacity, the more stuff you can keep on your PC. Cloud-based (Internet) storage may be good for housing files you plan to share among your phone, tablet, and PC, but local storage is less expensive, and you only have to buy it once.

Speed: This is where SSDs shine. An SSD-equipped PC will boot in less than a minute, and often in just seconds. A hard drive requires time to speed up to operating specs, and will continue to be slower than an SSD during normal use. A PC or Mac with an SSD boots faster, launches and runs apps faster, and transfers files faster. Whether you're using your computer for fun, school, or business, the extra speed may be the difference between finishing on time and failing.

Fragmentation: Because of their rotary recording surfaces, hard drives work best with larger files that are laid down in contiguous blocks. That way, the drive head can start and end its read in one continuous motion. When hard drives start to fill up, large files can become scattered around the disk platter, causing the drive to suffer from what's called fragmentation. While read/write algorithms have improved to the point that the effect is minimized, hard drives can still become fragmented. SSDs can't, however, because the lack of a physical read head means data can be stored anywhere. Thus, SSDs are inherently faster.

Durability: An SSD has no moving parts, so it is more likely to keep your data safe in the event you drop your laptop bag or your system is shaken about by an earthquake while it's operating. Most hard drives park their read/write heads when the system is off, but they are flying over the drive platter at a distance of a few nanometers when they are in operation. Besides, even parking brakes have limits. If you're rough on your equipment, an SSD is recommended.

Availability: Hard drives are more plentiful in budget and older systems, but SSDs are becoming more prevalent in recently released high-end laptops like the Apple MacBook Pro, which does not offer HDDs even as a configurable option. Desktops and cheaper laptops, on the other hand, will continue to offer HDDs, at least for the next few years.

Form Factors: Because hard drives rely on spinning platters, there is a limit to how small they can be manufactured. There was an initiative to make smaller 1.8-inch spinning hard drives, but that's stalled at about 320GB, since the phablet and smartphone manufacturers have settled on flash memory for their primary storage. SSDs have no such limitation, so they can continue to shrink as time goes on. SSDs are available in 2.5-inch laptop drive-sized boxes, but that's only for convenience.

Noise: Even the quietest hard drive will emit a bit of noise when it is in use from the drive spinning or the read arm moving back and forth, particularly if it's in a system that's been banged about or if it's been improperly installed in an all-metal system. Faster hard drives will make more noise than those that are slower. SSDs make virtually no noise at all, since they're non-mechanical.

Power: An SSD doesn't have to expend electricity spinning up a platter from a standstill. Consequently, none of the energy consumed by the SSD is wasted as friction or noise, rendering them more efficient. On a desktop or in a server, that will lead to a lower energy bill. On a laptop or tablet, you'll be able to eke out more minutes (or hours) of battery life.

Longevity: While it is true that SSDs wear out over time (each cell in a flash memory bank can be written to and erased a limited number of times), thanks to TRIMcommand technology that dynamically optimizes these read/write cycles, you're more likely to discard the system for obsolescence (after six years or so) before you start running into read/write errors with an SSD. If you're really worried, there are several tools that will let you know if you're approaching the drive's rated end of life. Hard drives will eventually wear out from constant use as well, since they use physical recording methods. Longevity is a wash when it's separated from travel and ruggedness concerns.

Overall: Hard drives win on price, capacity, and availability. SSDs work best if speed, ruggedness, form factor, noise, or fragmentation (technically part of speed) are important factors to you. If it weren't for the price and capacity issues, SSDs would be the hands-down winner.

## The Right Storage for You

So, does an SSD or HDD (or a hybrid of the two) fit your needs? Let's break it down:

HDDs

• Enthusiast multimedia users and heavy downloaders: Video collectors need space, and you can only get to 4TB of space cheaply with hard drives.

• Budget buyers: Ditto. Plenty of cheap space. SSDs are too expensive for $500 PC buyers.

• Graphic arts and engineering professionals: Video and photo editors wear out storage by overuse. Replacing a 1TB hard drive will be cheaper than replacing a 500GB SSD.

• General users: General users are a toss-up. Folks who prefer to download their media files locally will still need a hard drive with more capacity. But if you mostly stream your music and videos online, then buying a smaller SSD for the same money will give you a better experience.

SSDs

• Road warriors: People who shove their laptops into their bags indiscriminately will want the extra security of an SSD. That laptop may not be fully asleep when you violently shut it to catch your next flight. This also includes folks who work in the field, like utility workers and university researchers.

• Speed demons: If you need things done now, spend the extra bucks for quick boot-ups and app launches. Supplement with a storage SSD or hard drive if you need extra space (see below).

• Graphic arts and engineering professionals: Yes, we know we said they need hard drives, but the speed of an SSD may make the difference between completing two proposals for your client and completing five. These users are prime candidates for dual-drive systems (more on that below).

• Audio engineers and musicians: If you're recording music, you don't want the scratchy sound from a hard drive intruding. Go for quieter SSDs.

## Hybrid Drives and Dual-Drive Systems

Back in the mid 2000s, some hard drive manufacturers, like Samsung and Seagate, theorized that if you add a few gigabytes of flash chips to a spinning hard drive, you'd get a so-called "hybrid" drive combining a hard drive's large storage capacity with the performance of an SSD, at a price only slightly higher than that of a typical hard drive. The flash memory acts as a buffer for frequently used files, so your system has the potential for booting and launching your most important apps faster, even though you can't directly install anything in that space yourself. In practice, hybrid drives work, but they are still more expensive and more complex than regular hard drives. They work best for people like road warriors who need both lots of storage and fast boot times. Since they're an in-between product, hybrid drives don't necessarily replace dedicated hard drives or SSDs.

In a dual-drive system, the manufacturer will install a small SSD primary drive (C:) for the operating system and apps, and add a larger spinning hard drive (D: or E:) for storing files. This works well in theory; in practice, manufacturers can go too small on the SSD. Windows itself takes up a lot of space on the primary drive, and some apps can't be installed on other drives. Some capacities may also be too small. For example, you can install Windows 10 on an SSD as small as 16GB, but there will be little room for anything else. In our opinion, 120GB to 128GB is a practical minimum size for the C: drive, with 256GB or more being even better. Space concerns are the same as with any multiple-drive system: You need physical space inside the PC chassis to hold two (or more) drives.

Last but not least, an SSD and a hard drive can be combined (like Voltron) on systems with technologies like Intel's Smart Response Technology (SRT) or Apple's Fusion Drive. They use the SSD invisibly to act as a cache to help the system more speedily boot and launch programs. As on a hybrid drive, the SSD is not directly accessible by the end user. SRT requires true SSDs, like those in 2.5-inch form factors, but those drives can be as small as 16GB in capacity and still boost performance; since the operating system isn't being installed to the SSD directly, you avoid the drive space problems of the dual-drive configuration mentioned above. On the other hand, your PC will need space for two drives, a requirement that may exclude some laptops and small-form-factor desktops. Fusion Drive is only available on Mac desktops, for instance. You'll also need the SSD and your system's motherboard to support the caching technology for this scenario to work. All in all, however, it's an interesting workaround.

## The Storage of Tomorrow

It's unclear whether SSDs will totally replace traditional spinning hard drives, especially with shared cloud storage waiting in the wings. The price of SSDs is coming down, but they're still too expensive to totally replace the terabytes of data that some users have in their PCs and Macs. Cloud storage isn't free, either: You'll continue to pay as long as you want personal storage on the Internet. Local storage won't go away until we have reliable wireless Internet everywhere, including in planes and out in the wilderness. Of course, by that time, there may be something better.

Looking for some extra storage? Check out our list of the best external hard drives. Or if you want to protect or store your files online, check out our roundups of the best cloud storage and file-syncing services and the best online backup services.

# Applied physics: Record data storage

Nature volume466, page1024 (26 August 2010) | Download Citation

Appl. Phys. Lett. doi:10.1063/1.3463470 (2010)

Data have been recorded on a tiny slice of a metal oxide at a density eight times that offered by today's most advanced magnetic disk drives.

In magnetic data storage, data are written to disk by a magnetic read-and-write head that changes the magnetization of a region a few hundred nanometres across. One option for boosting memory in ever-shrinking electronics is to use ferroelectric materials, in which data can be encoded in the polarization of smaller regions.

Kenkou Tanaka and Yasuo Cho at Tohoku University in Sendai, Japan, recorded 64 × 64 bits of real data at a spacing of 12.8 nanometres per bit on a crystalline slice of lithium tantalate. This amounts to a density of 0.6 trillion bits per square centimetre.

·         ADVANCED MATERIALS

·         RESEARCH UPDATE

# Organic ferroelectrics finally stick in the memory

24 Jul 2018 Robert Westbrook

Xiong Ren-Gen and Yu-Meng You with their students. Credit: Yu-Meng You and Xiong Ren-Gen

Inorganic ferroelectrics have promised to change the face of semiconductor electronics for almost a century, but high processing costs have so far limited development. Now, researchers at Southeast University in Nanjing, China, have paved the way for progress by fabricating the first metal-free perovskite crystals. They present a set of materials that can achieve the performance of inorganic ferroelectrics but with the versatility, low-cost and low-toxicity inherent in organics.

To induce the directional switching of polarization characteristic of ferroelectricity, a material must contain a spontaneous dipole that can respond to an electric field. In other words, the centres of positive and negative charge within a crystal must be different. For metal-free perovskites, this should theoretically happen when a highly symmetric non-ferroelectric state is ‘frozen’ into a state with polar symmetry.

The MDABCO molecule (bottom-left) and the perovskite structure with the central “A” site highlighted. Credit: Yu-Meng You and Xiong Ren-Gen

### From database to device

With this in mind, Ren-Gen Xiong and Yu-Meng You instructed their students to scour the hundreds of thousands of entries in the Cambridge Structural Database for molecules of suitable size and symmetry. Such candidates could then be incorporated into the traditionally metallic “A” site of the perovskite structure, yielding an all-organic perovskite ferroelectric.

The result of their efforts is the discovery of 23 metal-free perovskites including MDABCO-NH4I3 (MDABCO is N-methyl-N’-diazabicyclo[2.2.2]octonium). This particular crystal displayed a spontaneous polarization of 22 microcoulombs per centimetre square, close to that of the state-of-the-art perovskite ferroelectric, BaTiO3 (BTO). In addition, crystals can be formed readily at room temperature, avoiding the excessive heat (>1000 oC) required to make inorganic ferroelectrics. This will lower fabrication costs and open the door for more delicate device applications such as flexible devices, soft robotics and biomedical devices.

The MDABCO molecule is crucial to the large spontaneous polarization that the researchers observed. At high temperatures, excessive thermal energy leaves the MDABCO molecule in a state of free rotation within the crystal. Here, the average centres of positive and negative charge at the molecule site are the same and ferroelectricity is forbidden. However, when cooled below the phase transition temperature of 448 K, the MDABCO molecule becomes locked in place revealing a significant dipole with eight possible polarization directions.

### Beyond binary

Ferroelectric random access memory (Fe-RAM) works on the principle that individual cells are charged to states “0” and “1”, represented by different polarization directions of the active material.  As ferroelectric crystals tend to have two polarization states, we obtain the well-known binary system. The eight possible polarization directions in MDABCO-NH4I3 then, will pique the interest of those looking to make next-generation memory devices.

“In principle, eight polarization directions could be used to make an octonary device with eight different logic states”, explains Yu-Meng You. “This is a potential strategy for increasing the density of future RAM devices”. While You expresses concern over increased architectural complexity in such a device, the potential for cramming eight bits into a single cell could add to the commercial prospects of this set of materials.

READ MORE

Data storage prospects broaden for antiferromagnetics

### Prospects for perovskites

But the opportunities for advancement don’t stop at memory applications. “We have demonstrated a new system of perovskites with compositional flexibility, adjustable functionalization and low toxicity. We expect the metal-free perovskite system will attract great attention in near future”.

Full details are reported in Science.

# https://spectrum.ieee.org/nanoclast/semiconductors/nanotechnology/single-atom-serves-as-worlds-smallest-magnet-and-data-storage-device

# Single Atom Serves as World's Smallest Magnet and Data Storage Device

## For the first time, a single atom can store a single bit of data

By Dexter Johnson

Photo: IBM Research - AlmadenDr. Christopher Lutz of IBM Research - Almaden in San Jose, Calif. with IBM Research's Nobel-prize winning microscope he used to store data on a single-atom magnet.

Advertisement

An international team of researchers have produced the world’s smallest magnet and demonstrated that it’s possible to use that magnet—an individual atom—to store a single bit of data.

Until this latest research, led by teams at IBM Research Almaden and École Polytechnique Fédérale de Lausanne (EPFL) in Switzerland, molecules were the smallest-ever data storage units. To put this advance in context, think about it like this: With one bit per atom, it would be conceivable to store an entire iTunes library of 35 million songs on a device no bigger than a credit card.

This latest result stems from work about which we reported on 6 March: IBM Research Almaden developed an electron-spin resonance (ESR) sensor consisting of a single iron atom on the tip of a scanning tunneling microscope(STM). STMs detect the tunneling of electrons between the ultra-sharp probe as it’s scanned across a surface, when it is combined with the iron atom it can measure the magnetic field of an atom more directly and with greater sensitivity than any other method.

Now we know what the scientists have been using their newly developed iron-atom sensor for: to detect the magnetic fields of holmium atoms. The holmium atom comes from a family of rare earth metals that are known for their high level of magnetism. Prior to the development of the iron-atom sensor, there didn’t appear to be a way to both read and manipulate the magnetic pole of the holmium atoms using only an STM without disrupting it.

By being able to read the holmium atoms magnetic pole (north or south) with the iron atom, the holmium atom can be used to store the zeros and ones used in digital logic. In essence, the researchers have developed a read-write method for storing data on a single atom with the combination of an STM with an iron atom that serves as an ESR sensor.

In the latest research described in the journal Nature, the researchers found that they could place the iron atom within a nanometer of the holmium atom so that the iron atom could read the north and south of its magnetic poles (the 0 and 1 of digital logic) without the sensor atom being affected by the electrical current that turns the holmium atom’s magnetic state from north to south. Because the iron and holmium atoms can be so closely spaced, it’s conceivable that engineers could create magnetic storage that is a thousand times as dense as today’s hard disk drives and solid state memory chips.

In the video below, some history of the STM is provided, along with how, in this case, it helps serve as a read-write data storage system for single atoms.

The arrangement of this single-atom, read-write memory storage system starts by placing the atoms on a substrate of magnesium oxide that serves as an insulating layer between the metal electrodes beneath it and the magnetic atoms on top of it. The holmium atom—which will hold its polarization for a long time under many conditions including the presence of magnets, making it ideal as a data storage medium—is attached to this magnesium oxide surface.

When the tip of the STM introduces current to the holmium atom, it flips the magnetic north and south poles of the atom, changing its state from 1 to 0 or vice versa. This step more or less corresponds to the “write” process in a hard disk drive.

The “read” process involves the iron atom detecting the magnetic state of the holmium atom. This achieved by exploiting a phenomenon known “precess.” When atoms that have unpaired electron spins are placed in a magnetic field, they rotate around the magnetic field at a precise frequency. This frequency depends on the field strength and the atom's magnetic moment, which is the strength of the atom's magnetism.

The researchers apply a magnetic field to the microscope and then a high-frequency voltage to the tunnel junction of the STM. When the frequency of the voltage matches the frequency of the spin precession, the spin is driven away from its thermal equilibrium, which is primarily aligned with the magnetic field. The iron sensor on the tip of the STM detects this change in orientation because the frequency sweeps through the resonance frequency, making for a sharp change in tunnel current that appears exactly at the resonant frequency. This resonance frequency moves in response to nearby magnetic atoms.

“The physical principle is the same as for magnetic resonance imaging, except that we detect electron precession instead of nuclear precession, and we address individual atoms instead of billions of them, by positioning the tip over the atom of interest,” Chris Lutz, staff scientist at IBM Almaden, explained to IEEE Spectrum earlier this week.

Lutz cautions that we shouldn’t expect this technology to replace our computer hard-disk drives anytime soon. The STMs that perform this work have to be kept at four degrees Kelvin in order to keep the atoms from moving around, which obviously is not going to be possible for a mobile handset in your pocket. There is also a long list of scientific and engineering steps that loom ahead, such as manufacturability.

IBM Almaden STM Lab

That said, Lutz and his team are clearly enthusiastic about the prospects that this latest line of research has turned up. A few years ago, they looked at this class of magnetic atoms only to be disappointed that they couldn’t do much with them because their electron structure made it difficult for the STMs to work with them.

But now, with the discovery of their new ESR sensor in the form of a single iron atom, the possibilities seem endless. It’s too early to tell whether it will ultimately lead to a new type of computer data storage. But the journey might yield many more breakthroughs than just computer memory.